## Slide 1
HAZEL Webinar 2:
Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
6th October 2020
Place image in this area.

## Slide 2: Decentralized hydrogen production from green methane – The Reformer Steam Iron Cycle (RESC)
Sebastian Bock, Karin Malli, Michael Lammer and Viktor Hacker
Institute of Chemical Engineering and Environmental Technology
Graz University of Technology, Austria
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks

## Slide 3
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Introduction
High-purity hydrogen from biogas Decentralized PEMFC-grade hydrogen
On-Site hydrogen with Negative Emissions Sequestration of pure CO2
100 bar hydrogen release Pre-pressurized H2 release
Conclusion and Outlook
Outline

## Slide 4
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
2000 2010 2020 2023
Fundamental research
0.5 kW lab reactor
Publication of RESC
by Viktor Hacker
10 kW lab reactor
Foto: © Lammer / TU Graz
Foto: © Lammer / TU Graz
H2 from
real producer biogas
Foto: © Bock / TU Graz
Foto: © Lunghammer / TU Graz
Foto: © TU Graz
The Reformer Steam Iron Cycle (RESC)

## Slide 5
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Introduction Motivation and challenges
Hydrogen from locally available resources
Decentralized hydrogen generation is environmentally friendly
Regional feedstock utilization
Efficient and cost-effective conversion
Stringent restrictions on hydrogen quality for low-temperature PEM-FC

## Slide 6
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Introduction RESC process as hydrogen production pathway

## Slide 7
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Outline
Introduction
High-purity hydrogen from biogas Decentralized PEMFC-grade hydrogen
On-Site hydrogen with Negative Emissions Sequestration of pure CO2
100 bar hydrogen release Pre-pressurized H2 release
Conclusion and Outlook

## Slide 8
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Introduction RESC process as hydrogen production pathway
HYDROGEN

## Slide 9
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Advances in 10 kW lab system Lab demonstration system
Reproduced from: Bock et al., 2019, DOI:10.1039/C9RA03123E Published by The Royal Society of Chemistry under CC BY 3.0

## Slide 10
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Advances in 10 kW lab system Hydrogen storage and long-term experience
1000 hours time-on-stream, over one year of discontinuous operation
Loss-free energy storage with an energy density equal to 700 bar PH2
Up to 65% feedstock utilization for high-purity H2 - 99.999%
On-time hydrogen generation e.g. for decentralized systems

## Slide 11
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Outline
Introduction
High-purity hydrogen from biogas Decentralized PEMFC-grade hydrogen
On-Site hydrogen with Negative Emissions Sequestration of pure CO2
100 bar hydrogen release Pre-pressurized H2 release
Conclusion and Outlook

## Slide 12
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Pure hydrogen, carbon dioxide and nitrogen sequestration from biogas feed
Reproduced from: Bock et al., 2020, DOI: 10.1039/C9SE00980A Published by The Royal Society of Chemistry under CC BY 3.0

## Slide 13
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Pure hydrogen, carbon dioxide and nitrogen sequestration from biogas feed
Adapted from: Bock et al., 2020, DOI: 10.1039/C9SE00980A Published by The Royal Society of Chemistry under CC BY 3.0
1: Methane, O/R ratio 1.2
2: Biogas, 25% CO2, O/R ratio 1.2
3: Biogas, 25% CO2, O/R ratio 1.6

## Slide 14
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Pure hydrogen, carbon dioxide and nitrogen sequestration from biogas feed
Adapted from: Bock et al., 2020, DOI: 10.1039/C9SE00980A Published by The Royal Society of Chemistry under CC BY 3.0
1: Methane, O/R ratio 1.2
2: Biogas, 25% CO2, O/R ratio 1.2
3: Biogas, 25% CO2, O/R ratio 1.6

## Slide 15
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Adapted from: Bock et al., 2020, DOI: 10.1039/C9SE00980A Published by The Royal Society of Chemistry under CC BY 3.0
Pure hydrogen, carbon dioxide and nitrogen sequestration from biogas feed

## Slide 16
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Outline
Introduction
High-purity hydrogen from biogas Decentralized PEMFC-grade hydrogen
On-Site hydrogen with Negative Emissions Sequestration of pure CO2
100 bar hydrogen release Pre-pressurized H2 release
Conclusion and Outlook

## Slide 17
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
100 bar high-pressure hydrogen Pre-pressurized H2 release
System-integrated 100 bar pre-pressurized release by liquid feed water compression
Significant energy savings for 1000 bar allocation
Reprinted from: Zacharias et al., 2019, Int. J Hydrogen Energy, DOI:10.1016/j.ijhydene.2019.01.257 under CC BY-NC-ND 4.0

## Slide 18
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Outline
Introduction
High-purity hydrogen from biogas Decentralized PEMFC-grade hydrogen
On-Site hydrogen with Negative Emissions Sequestration of pure CO2
100 bar hydrogen release Pre-pressurized H2 release
Conclusion and Outlook

## Slide 19
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Conclusion
Decentralized PEM-FC grade hydrogen from renewable resources
  Excellent gas purity (99.999%)
  Feedstock utilization up to 65%
  Zero- or negative carbon dioxide emissions with CCS/CCU
  Loss-free energy storage for peak coverage
  On-demand hydrogen
Pre-pressurized release at 100 bar

## Slide 20
The project Bio-LOOP is funded by the Austrian Federal Ministry for Climate Action, Environment, Energy, Mobility, Innovation and Technology (BMK) and the Austrian Research Promotion Agency (FFG). It is supported by the COMET-Module and BEST - Bioenergy and Sustainable Technologies GmbH.
The financial support of the project Biogas2H2 by the Austrian Klima- and Energiefonds through the Energy Research Program 2015 is gratefully acknowledged.
Funding organizations
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Acknowledgements

## Slide 21
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Project H2GreenTECH
Strengthening crossborder R&I capacities in advanced hydrogen technologies by developing synergies between enterprises, R&D centers and higher education
Duration: 01.03.2020 – 31.08.2022
Project budget: 584.500,00 EUR
Better access and use of research infrastructure
Build-up of competences of enterprises, R&D centres and higher education
Development of the cross border Roadmap
One-Stop-Shop
H2 Center
national public authority
interest groups SME, NGOs
higher education & research

## Slide 22
HAZEL Webinar 2: Hydrogen Sustainability - H2 DXNET - Hydrogen injection into natural gas distribution networks
Contact
Working Group Fuel Cell and Hydrogen Systems
Institute of Chemical Engineering & Environmental Technology Graz University of Technology, Austria
Open Access: R. Zacharias, S. Bock, V. Hacker, The impact of manufacturing methods on the performance of pelletized, iron-based oxygen carriers for fixed bed chemical looping hydrogen in long term operation, Fuel Process. Technol. 208 (2020) 106487. https://www.doi.org/10.1016/j.fuproc.2020.106487
Open Access: S. Bock, R. Zacharias, V. Hacker, Co-production of pure hydrogen, carbon dioxide and nitrogen in a 10 kW fixed-bed chemical looping system, Sustain. Energy Fuels. 4 (2020) 1417–1426. https://doi.org/10.1039/C9SE00980A
Open Access: Bock, S., Zacharias, R., & Hacker, V. (2019). Experimental study on high-purity hydrogen generation from synthetic biogas in a 10 kW fixed-bed chemical looping system. RSC Advances, 9(41), 23686–23695. https://doi.org/10.1039/C9RA03123E
Open Access: Zacharias, R., Visentin, S., Bock, S., & Hacker, V. (2019). High-pressure hydrogen production with inherent sequestration of a pure carbon dioxide stream via fixed bed chemical looping. International Journal of Hydrogen Energy, 44(16), 7943–7957. https://doi.org/10.1016/j.ijhydene.2019.01.257
Open Access: Nestl, S., Voitic, G., Zacharias, R., Bock, S., & Hacker, V. (2018). High-Purity Hydrogen Production with the Reformer Steam Iron Cycle. Energy Technology, 6(3), 563–569. https://doi.org/10.1002/ente.201700576
Open Access: Voitic, G., Hacker, V., (2016). Recent advancements in chemical looping water splitting for the production of hydrogen. RSC Advances, 6(100), 98267–98296. https://doi.org/10.1039/C6RA21180A
Open Access: Voitic, G., Nestl, S., Malli, K., Wagner, J., Bitschnau, B., Mautner, F. A., & Hacker, V. (2016). High purity pressurised hydrogen production from syngas by the steam-iron process. RSC Advances, 6(58), 53533–53541. https://doi.org/10.1039/c6ra06134f