## Slide 1: Hydrogen Exploring Opportunities in the Northern Ireland Energy Transition
Dr Rory Monaghan
Ryan Institute Energy Research Centre, School of Engineering, NUI Galway
MaREI, the SFI Centre for Energy, Climate and Marine Research
11 November 2020

## Slide 2: Background
NI Department for the Economy commissioned NUI Galway, with partners Dublin City University and HyEnergy Consulting, to prepare a report on the opportunities for Northern Ireland in hydrogen.
This webinar seeks input from key stakeholders for the final report.
Your further input is very welcome. Please email rory.monaghan@nuigalway.ie with the subject line “Northern Ireland Hydrogen”.

## Slide 3: Overview
Key Technologies & Applications for NI
Enabling Policies in UK, ROI & EU
2030 Hydrogen Scenarios
Outlook

## Slide 4: Key Technologies & Applications
Production
  Electrolysers
  Steam Methane Reforming (with & without CCUS)
Storage & Transportation
  Pressurised gas
  Cryogenic liquid
  Hydrogen-containing liquids
End use
  Existing gas-burning appliances (boilers, engines, gas turbines)
  Industrial feedstock
  Fuel cells
Electrolyser
Steam Methane Reformer
Water
Electricity
Water
Natural gas
Carbon capture
CO2
Production
Oxygen
Hydrogen
Hydrogen

## Slide 5: Key Technologies & Applications
Production
  Electrolysers
  Steam Methane Reforming (with & without CCUS)
Storage & Distribution
  Pressurised gas
  Cryogenic liquid
  Hydrogen-containing liquids
End use
  Existing gas-burning appliances (boilers, engines, gas turbines)
  Industrial feedstock
  Fuel cells
Electrolyser
Steam Methane Reformer
Water
Electricity
Water
Natural gas
Carbon capture
CO2
Compressor
High-press cyl
Nat. gas grid
Salt cav-erns
Liquefaction
Cryo liq. tanks
Chemical transformation
Liquid tanks
Storage & Distribution
Production
Oxygen
Hydrogen
Hydrogen

## Slide 6: Key Technologies & Applications
Production
  Electrolysers
  Steam Methane Reforming (with & without CCUS)
Storage & Distribution
  Pressurised gas
  Cryogenic liquid
  Hydrogen-containing liquids
End use applications
  Existing gas-burning appliances (boilers, engines, gas turbines)
  Industrial feedstock
  Fuel cells
Electrolyser
Steam Methane Reformer
Water
Electricity
Water
Natural gas
Carbon capture
CO2
Compressor
High-press cyl
Nat. gas grid
Salt cav-erns
Liquefaction
Cryo liq. tanks
Chemical transformation
Liquid tanks
Transport
Trans & Storage
Heating
Power
Ind. Feed.
Blended ICEs, fuel cells
Long-term, high-capacity
Boilers, fuel cells (for CHP)
Blended GTs, fuel cells
Chem, steel, others
End Use Applications
Storage & Distribution
Production
Oxygen
Hydrogen
Hydrogen

## Slide 7: Key Technologies & Applications
Production
  Electrolysers
  Steam Methane Reforming (with & without CCUS)
Storage & Distribution
  Pressurised gas
  Cryogenic liquid
  Hydrogen-containing liquids
End use applications
  Existing gas-burning appliances (boilers, engines, gas turbines)
  Industrial feedstock
  Fuel cells
Electrolyser
Steam Methane Reformer
Water
Electricity
Water
Natural gas
Carbon capture
CO2
Compressor
High-press cyl
Nat. gas grid
Salt cav-erns
Liquefaction
Cryo liq. tanks
Chemical transformation
Liquid tanks
Transport
Trans & Storage
Heating
Power
Ind. Feed.
Blended ICEs, fuel cells
Long-term, high-capacity
Boilers, fuel cells (for CHP)
Blended GTs, fuel cells
Chem, steel, others
End Use Applications
Storage & Distribution
Production
Oxygen
Hydrogen
Hydrogen

## Slide 8: Electrolysers
System that splits water to hydrogen and oxygen
Input water needs to be pure but can be sourced via mains, bore holes or desalination processes
Produced hydrogen can be compressed, stored and shipped to power a variety of applications
If electricity is renewable, HYDROGEN IS GREEN
Scale up
Electrolysis has been widely accepted through Europe as a leading method to fight CO2 emissions
Gigawatts (GWs) of electrolysers are being planned around the globe
UK also has large systems planned i.e. 1.8 GW for the Zero Teesside initiative

## Slide 9: Steam Methane Reforming (SMR)
SMR technology splits natural gas (NG) into mixture of hydrogen, CO and CO2
Industries use SMR technology to deliver large quantities of H2 and CO with remaining CO2 being released to atmosphere
The process is mature with systems capable of producing up to 100s of metric tonnes per day of H2/CO
Currently over half the worlds hydrogen is derived from NG feedstocks

## Slide 10: SMR and Carbon Capture Utilisation and Storage (CCUS)
Capturing the CO2 produced by SMR can decarbonise the process
Captured CO2 can be stored in underground geological features or used
If CO2 is captured/used, HYDROGEN IS BLUE
Many large scale CCUS projects are being developed, and the UK is seeking to become world leading in CCUS technology.
The Acorn Project will capture about 200,000 tonnes of CO2 from the St Fergus Gas Terminal

## Slide 11: Salt Caverns for Gas Storage
Used to store gases including hydrogen since the 1950s
Sites have traditionally been developed after salt extraction by the chlorine industry
Over 30 caverns in use in the UK today
  mainly used for NG
  1 in use for hydrogen
  internal wall properties prevent leakage and contamination of the hydrogen
Lowest cost direct storage mechanism for large hydrogen volumes
Possibility to use Larne salt caverns for hydrogen storage

## Slide 12: Renewable Hydrogen in Mobility & Transport
Application | Status/Examples | Advantages | Disadvantages
Cars & vans | 11,000+ vehicles in California, Japan, Europe | Short refuelling time High energy density (v Li-ion) Long range (v Li-ion) Zero tailpipe emissions Low material footprint | Low network efficiency H2: Chicken and egg P2L: High cost NH3: Hazardous
Trucks & buses | Early commercial technologies 25,000 forklifts, 900 buses & trucks, including Aberdeen, Belfast & Dublin |  | 
Rail | Trains in Germany, UK, Austria & Netherlands | Low cost zero emissions for low utilisation lines | Many lines already electrified
Maritime | Small demonstration projects | H2 & NH3: Zero exhaust emissions Very few other options | Low energy density (v liquids)
Aviation | Small demonstration projects | P2L: High energy density Long range High value use for biomass | P2L: High cost H2: Fuel tank & airframe redesign

## Slide 13: EU Position on Hydrogen
European Commission “A Hydrogen Strategy for a Climate-Neutral Europe”, 2020. https://ec.europa.eu/energy/sites/ener/files/hydrogen_strategy.pdf

## Slide 14: Policy – UK and EU
UK government primary targets:
  Reduction in carbon emissions
  Hydrogen Mobility
  Utilising and promoting the use of British solutions
  Job creation and skills development
  Green hydrogen with substantial blue hydrogen use
EU and other regions primary targets:
  Reduction in carbon emissions
  Hydrogen Mobility
  Energy Diversity and Security
  Foster regional economic growth
  Green hydrogen almost exclusively, with other technologies to help transition
2020 has seen release of Hydrogen policies and roadmaps in France, Germany, Netherlands & Portugal
  UK and Ireland (due 2021) are lagging behind which has a knock-on effect on Northern Ireland
  How will Northern Ireland’s policy be shaped by the regions surrounding them?
Market Development
Rapid Market Delivery/Uptake
Market Rationalisation
2020
2030
2040
2050

## Slide 15: All-Island Potential
Both Ireland and Northern Ireland have enormous untapped renewable energy resources
Modern, increasingly interconnected electricity grid can accommodate high RES-E & SNSP
The modern, shared interconnected gas grid can be primed for hydrogen injection at a relatively low cost
  Reduce reliance on imported fuels and help bring household expenditure on energy down (NI has highest UK regional cost)
  Shared codes and standards
  Shared storage systems
Shared mobility infrastructure projects?
  Hydrogen refuelling stations both sides of the border
  Enables island-wide transportation corridors
  Renewal of rail rolling stock with H2 trains
EUCO scenarios suggests Ireland will be utilising only 2% of renewable energy generation potential in 2030!
Notes:   UK has committed to spending another £2.5 billion
  through the clean growth grand challenge to support
  low carbon innovation through to 2021.
  UK already has offered feed-in tariffs for biomethane
  under the non-domestic renewable heat incentive
  scheme – hydrogen could be next.

## Slide 16: 2030 Hydrogen Scenarios
Scenario 1: distributed H2 electrolysis, transport to nearest bus network or grid injection point

## Slide 17: 2030 Hydrogen Scenarios
Scenario 1: distributed H2 electrolysis, transport to nearest bus network or grid injection point
Scenario 2: Regional H2 electrolysis in Northwest, followed by:
2a: Transport to Derry/Londonderry to fuel 90 buses & 150 trucks
2b: Injection to natural gas grid to meet 10% of regional demand

## Slide 18: 2030 Hydrogen Scenarios
Scenario 1: distributed H2 electrolysis, transport to nearest bus network or grid injection point
Scenario 2: Regional H2 electrolysis in Northwest, followed by:
2a: Transport to Derry/Londonderry to fuel 90 buses & 150 trucks
2b: Injection to natural gas grid to meet 10% of regional demand
Scenario 3: Centralised H2 production near Belfast, followed by:
3a: Transport to Belfast to fuel 210 buses & 350 trucks
3b: Injection to natural gas grid to meet 10% of Greater Belfast demand

## Slide 19: Estimating Hydrogen Demand
Chart: Number of FCEV urban buses
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low | 3 | 5 | 7 | 10 | 15 | 20 | 30 | 45 | 60 | 75
Medium | 3 | 5 | 7 | 10 | 20 | 50 | 70 | 100 | 200 | 300
High | 3 | 5 | 7 | 20 | 50 | 70 | 100 | 200 | 300 | 600
Chart: Number of FCEV 40-tonne trucks
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low | 1 | 2 | 3 | 8 | 10 | 20 | 25 | 30 | 40 | 50
Medium | 1 | 2 | 3 | 10 | 50 | 100 | 150 | 200 | 300 | 500
High | 1 | 2 | 3 | 20 | 150 | 250 | 300 | 400 | 600 | 1000
Transport Sector
Projected number of FCEV urban buses in NI
70:30 split between Belfast & Derry
50,000 km per year
Projected number of FCEV 40-tonne trucks in NI
70:30 split between Belfast & Derry areas
100,000 km per year
Projections based on fleet turnovers, diesel bans, EU & HMI figures

## Slide 20: Estimating Hydrogen Demand
Chart: Number of FCEV urban buses
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low | 3 | 5 | 7 | 10 | 15 | 20 | 30 | 45 | 60 | 75
Medium | 3 | 5 | 7 | 10 | 20 | 50 | 70 | 100 | 200 | 300
High | 3 | 5 | 7 | 20 | 50 | 70 | 100 | 200 | 300 | 600
Chart: Number of FCEV 40-tonne trucks
| 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Low | 1 | 2 | 3 | 8 | 10 | 20 | 25 | 30 | 40 | 50
Medium | 1 | 2 | 3 | 10 | 50 | 100 | 150 | 200 | 300 | 500
High | 1 | 2 | 3 | 20 | 150 | 250 | 300 | 400 | 600 | 1000
Transport Sector
Natural Gas Use
Projected number of FCEV urban buses in NI
70:30 split between Belfast & Derry
50,000 km per year
Projected number of FCEV 40-tonne trucks in NI
70:30 split between Belfast & Derry areas
100,000 km per year
10% of 2019 gas consumption in Derry-Strabane and Causeway Coast & Glens (Scenario 2)
10% of 2019 gas consumption in Greater Belfast (Scenario 3)
Projections based on fleet turnovers, diesel bans, EU & HMI figures

## Slide 21
Supply
Production location?
Renewable sources?
Location?
Capacity?
Production capacity?
Centralised/ decentralised?
Gas grid
Demand
Applications and end-users?
Annual hydrogen demand?
Demand location?
Transport
Industry
Developing a Hydrogen Value Chain
For each scenario, we calculate capital & operating costs for hydrogen production, storage & transportation in the value chain.
Cost projections to 2030, transportation distances & economies of scale are included.
This gives a levelised cost per kg of delivered hydrogen for each scenario

## Slide 22: 2030 Hydrogen Scenarios - Results
Scenario | Value Chain Type | Location | Electricity Source | Demand Type | Optimum Electrolyser Capacity | Production Cost per kg H2 | Transport Cost per kg H2 | CO2 Savings
1 | Distributed | Throughout NI | Wind Farms | Various | 350 kW – 3.5 MW | £2.30 - £12 | £0.45 - £2.25 | n/a
2a | Regional | Derry | Grid | 90 buses, 150 trucks | 10 MW | £2.70 - £4.50 | £0.40 | 4,400 tCO2
2b | Regional | Northwest | Grid | 10% NW NG Demand | 14 MW | £2.60 - £4.40 | £0.00 | 2,800 tCO2
3a | Centralised | Belfast | Grid | 210 buses, 350 trucks | 23 MW | £2.50 - £4.40 | £0.10 | 10,300 tCO2
3b | Centralised | Greater Belfast | Grid | 10% Greater Belfast NG Demand | 94 MW | £2.40 - £4.20 | £0.00 | 18,500 tCO2

## Slide 23: 2030 Hydrogen Scenarios - Context
Transport scenarios
Scale & location are crucial to reduce production and transportation costs
Minimum delivered cost = £2.60/kg for Belfast
  Equivalent to 72p per litre of diesel
Bans on diesel-only buses in place in UK & ROI
RTFO could subsidise hydrogen production ~£5/kg if
  Electrolyser is connected directly to RES-E
  RES-E is purpose-built for hydrogen production
World’s first double-decker hydrogen fuel cell bus is designed and built in Northern Ireland
Hyundai Xcient hydrogen fuel cell 40-tonne truck has entered the European market (Switzerland)

## Slide 24: 2030 Hydrogen Scenarios - Context
Gas grid scenarios
Scale & location are crucial to reduce production and transportation costs
Minimum delivered cost = £2.40/kg for Belfast
  Equivalent to 7.2p/kWh
  Median NI domestic gas customer paid 4.8 p/kWh in H1 2019
Modern and growing gas grid in NI and ROI presents opportunities
Grid injection underway in GB (HyDeploy) and ROI (GNI blending site in Brownsbarn, Dublin)
Options for further in the future
  Blending at gas-fired power plants
  Storage in Larne salt cavern

## Slide 25: GenComm Ireland’s First Green Hydrogen Supply Chain
27-MW Long Mountain Wind Farm, Co Antrim
500-kW Areva electrolyser
2x 250-bar tube trailers
Bus fuelling depot, Belfast
3x Bamford Fuel Cell double-decker buses

## Slide 26: Outlook
Emission Reductions
Energy Diversity
Economic Benefits
What does this mean for Northern Ireland?
RES Expansion
H2 Tech testing ground
Northern Irish Expertise
Offset fossil fuel usage with H2
Potential Hydrogen Export to UK/ROI/EU
Skilled Job Creation – Manufacturing and O&M
Focus on hydrogen for heat and goods across Ireland
Reduce reliance on imported carbon fuels
New H2 applications to replace carbon-emitting processes
Utilise large renewables potential
Operational skills, expertise and added value
Historic manufacturing and fabrication
Ireland-wide gas grid injection
Prove viability of UK technology
Large green H2 Potential
Drivers
Opportunities

## Slide 27: Acknowledgements
Cian Moran & Arya Gunawan at NUI Galway
Jochelle Laguipo & Dr James Carton at Dublin City University
Josh Williamson, Tim Williamson, Diana Raine & Ian Williamson at HyEnergy Consulting
Paul McCormack at Belfast Metropolitan College
Meabh Cormacain & Eddie Kerr at the Department for the Economy
Your further input is very welcome. Please email rory.monaghan@nuigalway.ie with the subject line “Northern Ireland Hydrogen”.