## Slide 1
Place image in this area.
Green Hydrogen vs Electrification in Bus Fleets
A presentation of the
Enabling Support Tool
GenComm Partner Meeting #23
Tadgh Cummins, Tim Williamson

## Slide 2
H2 demand exists in some countries
Green H2 production potential exists in others
Its deployment will go hand in hand with renewables
Common question: “How much will green H2 cost?”
Europe’s H2 potential is immense

## Slide 3
Aimed to inform on quantities, costs, fossil fuel displacement for onshore green H2
GenComm’s Decision Support Tool
http://communityh2.eu/dst/
http://communityh2.eu/dst-simple/
Percentage of Dublin city bus fuel displaceable by H2 for different electrolyser operation modes
Hydrogen costs for different electricity prices and electrolyser operation modes, relative to diesel for Dublin

## Slide 4
Focus is now on specific sectors that:
Will struggle to be fully electrified
Have H2 technology close to or at commercial reality
We need to communicate to potential end-users in terms they understand
Cost effective decarbonization and energy security are the drivers, not finding a use for green H2!
What about the End User?
The Enabling Support Tool (EST)
Total Cost of Ownership (TCO) is how bus fleet operators VALIDATE decarbonization performance

## Slide 5
Enables bus fleet operators to plan best fleet decarbonization mix
Assumes first decarbonization approach will be battery electrification
Portion of routes in a network unsuited* to battery electrification are identified
* Due to HVAC loads, utilization rates, passenger & battery weight, steep gradients
The EST calculates Total Cost of Ownership of different decarbonization options
What does the EST do?

## Slide 6
Chart: Utilisation Rate (km/day)
| 100 | 125 | 150 | 175 | 175 | 176 | 200 | 225 | 250 | 275 | 300
ICEB | 1.1565 | 1.0713 | 1.0145 | 0.9739 | 0.97251 | 0.94347 | 0.9198 | 0.90087 | 0.88538 | 0.87247
Decarbonizing a single bus route in Galway
TCO drops as a bus is used more effectively
Diesel
Diesel

## Slide 7
Chart: Utilisation Rate (km/day)
| 100 | 125 | 150 | 175 | 175 | 176 | 200 | 225 | 250 | 275 | 300
BEB | 1.5165 | 1.2675 | 1.1015 | 0.9829 | 1.6944 | 1.6863 | 1.5165 | 1.3782 | 1.2675 | 1.1769 | 1.1015
ICEB | 1.1565 | 1.0713 | 1.0145 | 0.9739 | 0.97251 | 0.94347 | 0.9198 | 0.90087 | 0.88538 | 0.87247
Battery TCO drops quickly until…
Calculated battery maximum km/day
TCO drops as a bus is used more effectively
Diesel
Battery
Diesel
Decarbonizing a single bus route in Galway

## Slide 8
Chart: Utilisation Rate (km/day)
| 100 | 125 | 150 | 175 | 175 | 176 | 200 | 225 | 250 | 275 | 300
BEB | 1.5165 | 1.2675 | 1.1015 | 0.9829 | 1.6944 | 1.6863 | 1.5165 | 1.3782 | 1.2675 | 1.1769 | 1.1015
ICEB | 1.1565 | 1.0713 | 1.0145 | 0.9739 | 0.97251 | 0.94347 | 0.9198 | 0.90087 | 0.88538 | 0.87247
Battery
Battery TCO drops quickly until…
Calculated battery maximum km/day
Higher km/day needs more buses
Diesel
Battery
Diesel
Decarbonizing a single bus route in Galway

## Slide 9
Chart: Utilisation Rate (km/day)
| 100 | 125 | 150 | 175 | 175 | 176 | 200 | 225 | 250 | 275 | 300
BEB | 1.5165 | 1.2675 | 1.1015 | 0.9829 | 1.6944 | 1.6863 | 1.5165 | 1.3782 | 1.2675 | 1.1769 | 1.1015
ICEB | 1.1565 | 1.0713 | 1.0145 | 0.9739 | 0.97251 | 0.94347 | 0.9198 | 0.90087 | 0.88538 | 0.87247
FCEB | 1.5547 | 1.3315 | 1.1828 | 1.0765 | 1.0729 | 0.99681 | 0.93483 | 0.88524 | 0.84466 | 0.81085
Diesel
Battery
Calculated battery maximum km/day
Hydrogen is cost effective at higher km/day
Battery
Diesel
Hydrogen
Hydrogen
Battery is cost effective at lower km/day
Decarbonizing a single bus route in Galway

## Slide 10
EST Input process
Flat routes
Moderately hilly routes
Hilly routes
Very hilly routes
Select location from list
Input average operational hours per day
Maximum range of BEB is reduced
BEB range (km/day)
BEB range
BEB range
BEB range
BEB range
1
Buses can be input into four ‘hilliness’ categories:
2
3
Economic inputs: price of electricity, diesel, hydrogen
This input process circumvents the need for complex drive cycle inputs, while still capturing the essential fleet data required to compare & combine BEBs & FCEBs in a mixed fleet
Three bus sizes can be input:
Input number of buses below BEB range, and an average daily distance.
Repeat for buses below range of BEB
270 km/day
310 km/day
140 km/day
200 km/day
Model estimates worst-day energy demand of HVAC systems
110 km/day

## Slide 11
Galway city fleet
Flat routes
Moderately hilly routes
Hilly routes
Very hilly routes
Select location from list
Input average operational hours per day
Maximum range of BEB is reduced
BEB range (km/day)
BEB range: 254 km
BEB range
BEB range: 240 km
BEB range
1
Buses can be input into four ‘hilliness’ categories:
2
3
Economic inputs: price of electricity, diesel, hydrogen
Model estimates worst-day energy demand of HVAC systems
312 km/day
181 km/day
176 km/day
256 km/day
H2 | 8 | €/kg
Diesel | 1.66 | €/litre
Electricity | 0.22 | €/kWh
-19km

## Slide 12
Galway city fleet
Total Cost of Ownership
Total Cost of Abatement
BEB fleet requires +12 additional buses to maintain operations
BEB fleet peak charging station power of 1.1 MW
The mixed fleet of BEBs and FCEBs becomes the cheapest option after diesel at a hydrogen price of 8 – 9 €/kg*
* These are unpublished preliminary results

## Slide 13
Sensitivity Analysis

## Slide 14
Journal Paper
Journal paper in progress – “An Online Tool for Guiding Bus Fleet Decarbonisation through Green Hydrogen and Electrification”
Scenarios will be developed to investigate the shifting role of BEBs and FCEBs in bus fleets from 2023 to 2035 using prediction trends for the development of key parameters such as fuel/energy price, battery price, hydrogen infrastructure price and availability, and grid CO2 intensity

## Slide 15
Thank You