## Slide 1
NUI Galway Pilot and Irish Partners

## Slide 2
Koptekst
Pilot Location: Cloncrow
Bord na Mona site (Cavemount).
Dublin airport to Cloncrow ~1hr by car

## Slide 3
Pilot (Cloncrow),
Bord na Mona site (Cavemount).
NB: extent of degraded bog (C-potential!)

## Slide 4
Pilot: Cloncrow NHA,
Entire bog ~200 ha (blue)
Pilot site of ~26ha (white)
Active community group in Tyrellspass

## Slide 5
Private cutaway. Potential landowner involvement
Pilot site.
Drain blocking and monitoring with sphagnum transfer.
High Bog - Donor area
Coillte (State) Forestry
Potential involvement

## Slide 6
Pilot Site

## Slide 7
Investment WP I4 Cloncrow Bog
Owned by NPWS with state and private landownership:
Condition: Extensive Private cutaway, plus afforestation
Goals:
  Block drains in a 26ha pilot
  Instrument: Piezometers, env. Monitoring (soil temp, watertable, local rainfall & temp)
  Sphagnum transfer trials with cooperation with IPCC and community group ETHOS.
  Engage landowners in N.E. section for socio-economic or other trials
Total Bog: ~200ha | Pilot: 26 ha
Image source: RPSGroup

## Slide 8
Investment WP I4 Cloncrow Bog
Pilot Timelines:
Image source: RPSGroup
Activity | Date
Final Status Report & Initial Conditions | Jul-19
Joint Restoration Plan | Sep-19
Restoration Works | 20->21
Demonstrations | Jun-21
Spahgnum transfer workshop | Nov-21
Final Report | Jan-22

## Slide 9
Sub-Investment WP I4 – 503 ha
‘Associate’ pilot ~200ha (blue outline):
Former industrial bog
Needed to link main pilot to industrial emissions in same period, and we need monitoring at such sites.
BnM is interested in other PP pilots for potential use in their rehabilitation.
Cavemount Bog