## Slide 1
Workshop : GHG fluxes measurement plan
What? How? Where? When?
Sébastien Gogo

## Slide 2
Plan of the workshop
 Measurement plan in CARE PEAT
 The case of the Dutch site
 Discussion

## Slide 3
1.1. What and how do we measure?
The whole C budget of the ecosystem?
 very expensive, a lot of human ressources
 in CARE-PEAT focus on greenhouse gases CO2 and CH4 budget
Which technique?
 many techniques available (profiles, eddy covariance, chamber)
 in CARE-PEAT : chamber measurements
 CO2
 CH4
Los Gatos Research equipement

## Slide 4
1.1. What and how do we measure?
CO2
GPP
GPP : Gross Primary Production
ER : Ecosystem Respiration
NEE : Net Ecosystem Exchange
NEE > 0 : source system
NEE < 0 : sink system
ER
Ecosystem
Sol
NEE = ER – GPP

## Slide 5
1.1. What and how do we measure?
CH4
CO2
GPP
Ecosystem
Sol
GPP : Gross Primary Production
ER : Ecosystem Respiration
NEE : Net Ecosystem Exchange
NEE > 0 : source system
NEE < 0 : sink system
NEE = ER – GPP
ER

## Slide 6
1.1. What and how do we measure?
Time (s)
Time (s)
NEE = ER - GPP
Full light
ER
Dark
[CO2]
(ppm)
CO2
GPP
ER
CO2
ER
[CO2]
(ppm)

## Slide 7
1.1. What and how do we measure?
Use nets to have the light response of CO2 fluxes
Nets with different mesh
Ancillary variables, high frequency (1 hour min)
Water table depth
Air and soil temperature
Solar radiation
Vegetation % cove
Soil water content, if possible

## Slide 8
1.2. Where and when do we measure?
GHG budget before and after restoration works?
 not possible, need of many years timeseries
 in CARE-PEAT: focus on comparison between restored and control area to assess the effect of restoration actions on GHG budget
Measuring plots
Sub-area RESTORED #1
Sub-area RESTORED #2
Sub-area CONTROL #2
Sub-area CONTROL #1
Site
RESTORED area
CONTROL area
To better take into account the spatial heterogeneity

## Slide 9
1.2. Where and when do we measure?
La Guette
Control
Stripped + Sphagnum
SITE
AREA
SUB-AREA
Molinia
Erica
Sphagnum
Bare peat
REPLICATE
x3
x3
x3
x3
 French pilot
Measurement at what frequency?
 At least 12 campaigns
 1 light response curve per plot, per campaign

## Slide 10
1.3. To do what with the data?
From low frequency data to annual budget?
Chart: 
| 1 | 2 | 3 | 4 | 5
 | 2 | 5 | 15 | 8 | 3
Chart: 
| 1 | 2 | 3 | 4 | 5
 | 3 | 6 | 13 | 7 | 2
Chart: 
| 1 | 2 | 3 | 4 | 5
 | 2 | 7 | 22 | 30 | 33
Chart: 
| 1 | 2 | 3 | 4 | 5
 | 2 | 5 | 15 | 8 | 3
FLUX
Chart: 
| 1 | 2 | 3 | 4 | 5
 | 3 | 6 | 13 | 7 | 2
Variable
a) Time series from field campaigns
b) Models building
FLUX = a.VARIABLE + b
c) Variables measurement at high frequency
d) Calculation of high frequency flux time series
e) Integration of the fluxes to obtain the yearly GHG budget

## Slide 11
1.4. Modeling approach in CARE-PEAT
Methods and tools
UO, NUIG, MMU
All pilot managers
BRGM
WP T3
Model based on vegetation
All pilot managers
UO, NUIG, MMU
Decision Support Tool
BRGM
The whole consortium (associate partners)
WP LT
peatland managers

## Slide 12
2. The Dutch site
bare peat under water
natural succession towards Phragmites
bare peat under water and floating mats
natural succession
towards Phragmites
Peat
Water

## Slide 13
bare peat under water
natural succession towards Phragmites
bare peat under water and floating mats
natural succession
towards Phragmites
Peat
Water
What do we do?
2. The Dutch site