## Slide 1: GenComm 28 Nov 2019 Biomethane in Transport
Dr Peter Watters CEng FIMechE FIEI

## Slide 2: Biomethane in Transport
Introduction to Biomethane
Biogas Upgrade to Biomethane
Biomethane to Gas Grid
CNG Vehicle Refuelling
Renewable Fuel Obligation

## Slide 3: 1. Biomethane Costs
 | Density | Calorific Value | Pressure | Cost/Kg | Cost/kWh
Petrol | 0.75 | 46.7 | 0.5 | £1.60 | £0.12
Diesel | 0.83 | 43.1 | 100/250 | £1.71 | £0.14
LPG | 0.49 | 50.0 | 7 | £1.24 | £0.09
CNG | 0.17 | 55.0 | 250 | £0.72* | £0.05*
BioCNG | 0.17 | 55.0 | 250 |  | 
LNG | 0.40 | 55.0 | 3 | £1.00 | 
H2 (Gas) | 0.035 | 140.0 | 700/900 | £7.50 | £0.19
H2 (L) | 0.0708 | 140.0 | 11@-240C |  | N/A
WIP | Kg/Litre | MJ/Kg | Bar(g) | £/Kg | £/kWh

## Slide 4: 1. Biomethane - Benefits
NET Zero 2050
“UK and Ireland Governments 2019”
Climate Emergency
“Scotland, Wales, UK and Ireland, 28 Apr – 9 May 19”
Climate Change Hunger Striker
“Dail, 21 Nov 2019”
CNG/LNG versus Diesel -20% CO2 Reduction
Biomethane Versus Diesel -100% CO2 Reduction
“Volvo, Ballyclare 27 Nov 2019”

## Slide 5: 1. Biomethane – Renewable CNG
Natural Gas – Methane CH4
  Found in oil/gas deposits, Shale Gas (Unconventional)
  Un-sustainable, price independent of Oil
Renewable Natural Gas - Biomethane
  Anaerobic Digestion (with CO2)
  Land Fill gas (with CO2)
Transport applications
  LNG - Trucks and Ships
  CNG - Cars, Trucks and Buses

## Slide 6: 1. BioLNG

## Slide 7: 2. Biogas to Biomethane
Causeway Project
Vision 2050

## Slide 8: 2. Biogas to Biomethane
Anaerobic Digestion Biogas - Causeway Project
Reference | CH4 Min | CH4 Max | CO2 Min | CO2 Max | H2O Min | H2O Max | N2 Max | O2 Max | H2 Max | NH3 Max | H2S min | H2S Max
SEAI 04_11 | 50.0% | 75.0% | 25.0% | 45.0% | 2.0% | 7.0% | 2.0% | 2.0% | 1.0% | 1.0% | 20 | 20000

## Slide 9: 2. Biogas to Biomethane - Basics
Increase Pressure to 7 – 10 Bar.
Remove Impurities
  H2O
  H2S
  NH3
Separate or Vent CO2
Analyse, add Odorant (and Propane)

## Slide 10: 2. Biogas to Biomethane - Technology
Chemical addition into digester
Filters, Separators, Coalescers
CO2 removal (6 gas technologies)
  Cryogenic Separation < -78C
  Water Scrubbing
  Pressure Swing Absorption
  Chemical Treatment
  Amine Scrubbing
  Membrane Separation

## Slide 11: 3. Biomethane Gas 2 Grid
CRU approved & published on 15th Oct 18
Transcribed into the GNI Connection Policy V5.0
NFO
GNI

## Slide 12: 3. Biomethane Gas 2 Grid
Biomethane Producer (NFO) sells gas to Gas Grid
Gas Grid sells gas to the CNG station
UK Gas 2 Grid; 2017
GNI Gas 2 Grid; 2018/19 – Cush, County Kildare
N. Ireland - Q4, 2020 – UREGNI Work Plan 2019
Biomethane Producer sells into Biogas CHP Market
One Biomethane filling point in N. Ireland, “off-grid”

## Slide 13: 4. Biomethane Filling
CNG Filling – 2 Skids
  Natural Gas mains pressure 4 Bar
  CNG filling pressure 200/250 Bar to Vehicle UNECE R110
  ~ 90 kWe 500m3/hr 4 Stage Gas Compressor
    Electrical Supply
    Cooling of Compressor
  Buffer Gas Storage and cooling
  Standard Dispenser Standard Installation

## Slide 14: 4. Biomethane Filling

## Slide 15: 4. Biomethane Filling -
Who is going to build CNG/Biomethane Refuelling facilities?
“How much will a station cost?”
“How much do the trucks cost?”
Need to provide information to
Stakeholders, Stakeholders
Planners/HSE/Environment agency
Road Hauliers
Young people considering a long career in renewables

## Slide 16: 4. CNG Refuelling - Dublin

## Slide 17: 4. CNG

## Slide 18: 5. Renewable Transport Obligation
Renewable Transport Fuel Obligation
  Fuel supplier obliged to buy more renewables each year
  UK Government Policy in place, Biomethane certification
  Ireland Government – Consultation, 15 Nov 19
Value of a Renewable Transport Fuel Certificates
Market for certified Biomethane
Value to Biomethane producer
Work in Progress

## Slide 19: GenComm - Biomethane
Thank you
Belfast Metropolitan College; Paul & Joanna
Energia; Mark & Neil
Molgas; Ken
CNG Installations; Chris
IMechE; Patrick & Carlos
And everyone else!